## Slide 1: Analog Circuits and Systems
Prof. K Radhakrishna Rao
Lecture 12:
Static Characteristics of Feedback Systems

## Slide 2: Review
Feedback
Negative feedback and positive feedback
Desensitization in negative feedback systems
Inversion function
Feedback output follows the input
Error tends to zero as loop-gain tends to infinity
Voltage follower, current follower, phase follower, frequency follower
Square rooter from squarer, FM detector from FM generator, D to A converter from A to D converter,

## Slide 3: Offset in Feedback Systems
represents the forward transfer function of the system
If there is an offset at the output

## Slide 4: Negative feedback system with output offset
Offset at the output is reduced by (1+ Loop Gain)
Output offset can be compensated by suitably offsetting the input to the feedback system

## Slide 5: Non-linearity
Nonlinearities
Saturation
Input-output relationships of G1 and G2 are nonlinear
Most common non-linearity is Saturation and it is odd-symmetric in nature
When the output is saturated the feedback loop gets broken
The dynamic range of input signal Xi over which the feedback loop is functional is called ‘lock range’ of the feedback system

## Slide 6: Saturation
For small changes around a quiescent value the forward path gain function G1 may be approximated as the slope around the operating point
Saturation may be modeled as tanh function
an even symmetric function

## Slide 7: Saturation (contd.,)

## Slide 8: Negative feedback and Saturation
It is assumed that G2 is linear and there is no output offset
If saturation is simplified to include only the third order term

## Slide 9: Negative feedback and Saturation (contd.,)
As long as the error introduced due to saturation is negligible
For all values of Xi for which the output does not approach saturation limits, i.e., the incremental loop gain is greater than say 10, the error is reduced by a factor of
When output is in saturation the loop gain becomes zero and the loop is broken

## Slide 10: Example: Linear System
Gain = 10; G2 = 1/10; G10 = 100; System Saturates at +10 V

## Slide 11: Simulation
Input limit to saturation = +(10/10) = +1 V

## Slide 12: Simulation
For f = 1000 Hz
For input signal resulting in saturation

## Slide 13: Example: Feedback System with Offset
Saturation points at 0 and 20
Lock range of the system is 0 – 2 V

## Slide 14: Example
Piece-wise linear approximation to Nonlinear System
G2 = 1
G1 = 100 for
= 10 for
= 0 for
(Saturation)

## Slide 15: Example (contd.,)

## Slide 16: Simulation

## Slide 17: Simulation for low frequency inputs
For input signal not leading to saturation

## Slide 18: Simulation for low frequency inputs (contd.,)
For input signal resulting in saturation

## Slide 19: Lock Range: Divider
Multiplier is designed for inputs and outputs limited to + 10 V

## Slide 20: Lock Range: Square Rooter
As is always positive the lock range is given by 0 < Vi < 10

## Slide 21: Lock Range: Automatic Gain Controller

## Slide 22: Lock Range: Automatic Gain Controller (contd.,)
Vpo remains constant irrespective of changes in Vp, but depends on Vi
Vref has to remain positive for the loop to remain as negative feedback.
As multiplier output cannot be greater than 10 V; 0 < Vref <10
Lock range =

## Slide 23: Lock Range: Automatic Gain Controller (contd.,)
For the output tracks the input to the multiplier

## Slide 24: Simulation
In the lock range
Vp = 8V, VC = 5V

## Slide 25: Simulation
In the lock range
Vp = 10V, VC = 4V

## Slide 26: Simulation
Outside the lock range
Vp = 1V, VC is Saturated

## Slide 27: Lock Range: Current Amplifier
Trans-resistance amplifier cascaded with trans-conductance amplifier
G1 = 100kW x 10mS =1000 and G2 = 1/10
Output of Trans-resistance amplifier is limited to + 10V
Lock range of Ii is +10 mA

## Slide 28: Simulation

## Slide 29: Simulation
For Ii = 12 sin wt

## Slide 30: F-V in loop with V-F

## Slide 31: FLL – Lock Range

## Slide 32: Distortion caused by non-linearity

## Slide 33: Noise
Noise is any undesirable signal
Noise
may internally be generated in a system
can enter a system from external sources
Noise in electronics is broadly classified as
white noise (infinite bandwidth)
colored noise (narrow bandwidth)
shot noise (low frequency)
Drift in output offset

## Slide 34: Conclusion
Static characteristic of negative feedback systems
Distortion reduction
Linearity
Noise reduction
Effect of saturation
Dynamic range of operation or lock range
Dynamic characteristic of feedback loop will be the topic of next lecture